## Slide 1: 80 Build gem5-alddin/test_load_test
Peter H. Chen

## Slide 2: 80 Build gem5-alddin/test_load_test
Build Gem5-Alddin test_load_store
Below are the description of instructions to build the integration tests provided by Gem5-Aladdin Team Sam Xi.
gem5-cpu: Builds a version of the binary that runs on the CPU in gem5
gem5-accel: Builds a version of the binary that runs the accelerated function in Aladdin and the rest on the CPU.
gem: Builds both gem5-cpu and gem5-accel.
dma-trace-binary: Builds a version of the binary that is instrumented with LLVM-Tracer. Run this binary to generate a new dynamic_trace.gz. This binary is NOT meant to be simulated in gem5, so do not replace this with test_load_store - they serve completely different purposes.
https://github.com/harvard-acc/gem5-aladdin

## Slide 3: 80 Build gem5-alddin/test_load_store
Build Gem5-Alddin test_load_store
So, to rebuild and rerun a simulation of one of the integration tests:
> make clean
> make dma-trace-binary
> ./test_load_store-instrumented # This will generate a new dynamic_trace.gz
> make gem5-accel
> sh run.sh
https://github.com/harvard-acc/gem5-aladdin

## Slide 4: 80.1 make clean

## Slide 5: 80.1 make clean
Make clean
> ls
> make clean
https://github.com/harvard-acc/gem5-aladdin

## Slide 6: 80.1 make clean
Make dma-trace-binary
> ls -l
Before compile, we have
1. Makefile
2. test_load_store.c
3. gem5.cfg: Gem5 Configuration
4. test_load_store.cfg: test load and store configuration
5. run.sh: run the test
https://github.com/harvard-acc/gem5-aladdin

## Slide 7: 80.2 make dma-trace-binary

## Slide 8: 80.2 make dma-trace-binary
Make dma-trace-binary
> make dma-trace-binary
https://github.com/harvard-acc/gem5-aladdin

## Slide 9: 80.2 make dma-trace-binary
Make dma-trace-binary
> ls -l
https://github.com/harvard-acc/gem5-aladdin
dma trace binaries are generated:
1. full.llvm
2. full.s
3. lablemap
4. test_load_store-instrumented
5. test_load_store-opt.llvm
6. test_load_store.llvm

## Slide 10: 80.3 Generate Trace

## Slide 11: 80.3 Generate Trace
Generate Trace
We use instrumented binary to generate the dynamic trace
> ./test_load_store-instrumented # This will generate a new dynamic_trace.gz
https://github.com/harvard-acc/gem5-aladdin
On the right, we see the dynamic_trace.gz is generated.

## Slide 12: 80.4 Generate Gem5 Accelerator

## Slide 13: 80.4 Generate Gem5 Accelerator
Generate Gem5 Accelerator
> make gem5-accel
The gem5 accelerator is generated as below.
https://github.com/harvard-acc/gem5-aladdin

## Slide 14: 80.4 Generate Gem5 Accelerator
Generate Gem5 Accelerator
The test_load_store_gem5-accel is the compiled gem5/accelerator executable file.
copy test_load_store-gem5_accel into test_load_store
> cp test_load_store-gem5_accel test_load_store
https://github.com/harvard-acc/gem5-aladdin

## Slide 15: 80.5 Run run.sh

## Slide 16: 80.5 Run.sh
Run run.sh
> sh run.sh
https://github.com/harvard-acc/gem5-aladdin

## Slide 17: 80.6 Verify Result

## Slide 18: 80.7 Verify Aladdin Result
Verify Aladdin Result
> cd outputs
> cat test_load_summary
We have cycle: 2890 cycles, Avg Power: 22.8122 mW, and Total Area: 807763 uM^2
https://github.com/harvard-acc/gem5-aladdin

## Slide 19: 80.7 Calculate IPC (Instruction Per Cycle)

## Slide 20: 80.7 Calculate IPC (Instruction Per Cycle)
Calculate IPC (Instruction Per Cycle)
In the outputs directory
> vi stats.txt
We have number of instructions: 27648
https://github.com/harvard-acc/gem5-aladdin

## Slide 21: 80.7 Calculate IPC (Instruction Per Cycle)
Calculate IPC (Instruction Per Cycle)
We have cycles: 2890 cycles and number of instructions: 27648
IPC (Instruction per cycle) = 27648/2980 = 9.27785
https://github.com/harvard-acc/gem5-aladdin

## Slide 22: 80.8 Summary

## Slide 23: 80.8 Summary
Summary
IPC (Instruction per cycle) = 9.27785
Power: 22.8122 mW, and
Total Area: 807763 uM^2
https://github.com/harvard-acc/gem5-aladdin

## Slide 24: End